## Slide 1: Temperature Atmospheric Sciences 101 Winter 2019

## Slide 2: Temperature is a measure of the average speed of atoms and molecules

## Slide 3: Temperature
When a substance warms, atoms and molecules move faster.
In a solid, molecules remain bound together in a rigid crystalline structure
In a liquid, molecules are bound together but can move around.
In a gas, molecules move as independent entities

## Slide 5: Definition
Temperature is a measure of the average speed of atoms and molecules of a substance
More exactly, temperature is proportional to the average kinetic energy of a substances atoms and molecules
Kinetic Energy (KE) = (1/2)mv2, where m=mass, and v is speed
http://www.falstad.com/gas/fullscreen.html

## Slide 6: Temperature is measured with thermometers—and there are many types
Galileo developed the first thermometer in the late 1500s.

## Slide 7: Thermometer
In 1600s, alcohol thermometers came into use
In 1714, Gabriel Fahrenheit, a German physicist, constructed the first mercury thermometer.
A problem developed, different thermometers had different scales!
Promoted lots of confusion!

## Slide 8: Three Major Scales Used Today
Fahrenheit (°F)
Centigrade or Celsius (°C)
Kelvin or Absolute (°K, °A)
How to Convert Freezing Boiling
C=(5/9)(F-32) 0 100
F=(9/5)C + 32 32 212
K=C + 273 273 373
The rest of world uses C, only the US uses F

## Slide 9: Temperatures in Celsius (F)
100 (212F) boiling point of water at standard pressure
57 (134F) record high temperature (Libya)
50 (122F) typical summer high in Death Valley, CA
30 (86F) typical summer high over U.S. East Coast
20 (68F) normal room temperature
0 (32F) freezing
-10 (14F) super cold wave in Seattle
-40 (-40F) record cold in northern U.S.
-88 (-126F) record low temperature at South Pole
-273 (-460) absolute zero

## Slide 10: Types of Thermometers
The classic: hollow glass tube connected to a bulb filled with alcohol or mercury
Fluid expands or contracts as temperature changes
Fairly accurate. Typically good to about 1F.

## Slide 11
Alcohol and Mercury
Thermometers

## Slide 13: Bimetallic Strip Thermometers
2 different types of metals fused together
Different metals expand differently as temperature changes
Used in thermostats and cheap thermometers. Metal strips often in spirals.

## Slide 15: Electronic Thermometers
Often use thermisters, a device whose electrical resistance varies with temperature
Car thermometers, medical thermometers, etc.

## Slide 16: Radiometers
A device that measures the amount of radiation emitted by a substance
Amount and wavelength of radiation emitted is a function of temperature (warmer objects emit more and at shorter wavelengths)
Radiometers used by satellites to measure temperatures of clouds, atmosphere, and surface

## Slide 17: A radiometer you are familiar with

## Slide 18: One you may not be…

## Slide 19
GOES Weather Satellite

## Slide 20: Human Skin
With practice…good to roughly 2F.

## Slide 21: Official Surface Air Temperature Measurement
Always measured in the SHADE
Should be measured at 2-meters (about 6.6 ft) above surface.
Should be above grass or native vegetation

## Slide 22: Bad Exposure Can Produce Poor Observations

## Slide 23: How NOT to Get Dependable Temperatures

## Slide 24: Much Better

## Slide 25
Traditional Stevenson Screen

## Slide 26
Today: NOAA/NWS/FAA ASOS Temperature/Humidity
Senor

## Slide 27: Home Thermometer Tips
Put sensor on north side of the house/apartment IN PLACE THAT IS ALWAYS IN SHADE
Out of rain
Not above a BBQ!

## Slide 28: Why can knowing that temperatures are taken at 2-m save your life?

## Slide 29: Saving Your Life
On cold winter nights, temperature of the road surface can be 2-5F cooler than at 2 meters (or the 2 ft above the ground of your care thermometer)
Thus, when air temperatures get to around 35-37F here is the possibility that the road temperatures have dropped to freezing, with ice.
Slow down!

## Slide 30: Diurnal (Daily) Temperature Variations
When are temperatures generally warmest and coolest?

## Slide 31: Diurnal Temperature Variations
Minimum temperature generally just after sunrise
Max temps 3-4 hours after solar noon.
In Seattle, max temps are typically 2-3 PM in winter, 5-6 PM midsummer.

## Slide 32: Diurnal Amplitude Varies
Big Diurnal
Variations
In West Where
Air is Dry
Less
Diurnal
Variation
Where is
Is Moister

## Slide 33: All Temperatures Are Local
Temperatures can vary in small distances due to a number of factors:
  Proximity to water (cooler in summer, warmer in winter)
  Elevation (usually cooler aloft, but cool air can pool near the surface at night/winter)
  Surface characteristics/urban heat island (warmer in urban core)

## Slide 34: Urban Heat Island Can easily be 5-10F warmer in urban core

## Slide 35: London

## Slide 36: Elevation
During the night, cooler, denser air often drains into lower elevations

## Slide 37
Typical
Summer
Day
Near 5 PM

## Slide 38
Winter
Temps
Near 6 AM

## Slide 39: Snow Promotes Cooling Good in reflecting solar radiation, good emitter in infrared, good insulator Often record cold temperatures are associated with snow

## Slide 40: The Most Extreme Cold Locations Puts All of These Together
Valley
Snow
Away from water

## Slide 41
WA cold records are all east of the Cascades
On December 30, 1968 both Mazama and Winthrop, WA dropped to -48F—the state record.
Why there?

## Slide 42
Winthrop and Mazama are in a deep valley of the northeast Cascades
When snow on ground