## Slide 1: Update on OLYMPEX: A Ground Validation Field Campaign in the Pacific Northwest
Lynn McMurdie, Robert A. Houze, Jr., Jessica Lundquist, Cliff Mass, University of Washington, Walter Petersen NASA/Wallops, Mathew Schwaller NASA/Goddard.
PMM Science team presentation, Baltimore, 4 August, 2014

## Slide 2: Review of the goals of OLYMPEX
Physical validation of the precipitation (rain and snow) algorithms for both the GMI and DPR.
How precipitation mechanisms in midlatitude frontal systems and their modification by terrain affect GPM rainfall estimation uncertainties.
Quantifying the accuracy and uncertainty of the GPM precipitation data and its hydrologic applicability.
Merging numerical modeling and satellite observations to optimize precipitation estimation in hybrid monitoring systems of the future.

## Slide 3: To achieve these goals, we need to observe:
Upstream Conditions
  Meteorological conditions over the Pacific Ocean
Rain and Snow
  At multiple sites from coast, lowlands to mountain ridges
Microphysics
  Of precipitation in all sectors of midlatitude storms and variability in complex terrain
Brightband
  variability in height and over ocean, coastal, and mountain surfaces
Seasonal Snowpack
  In terms of SWE over the higher terrain
River
  Response and runoff
Emissivity
  Of a variety of surfaces: ocean, coast, forest and snow-covered mountains

## Slide 4: OLYMPEX meeting of 18-20 November 2013
Identified many ideas for measurements on the ground, by radar and aircraft.
Since the meeting…
Focused on the realistic possibilities ….

## Slide 5: Current state of the observational network
Existing observations: circles and diamonds
Enhanced observation sites: triangles
Radars: squares
Not shown: tipping bucket rain gauge network in the Quinault, other potential enhanced sites at Neilton Pt. and the Wynoochee, potential new SNOTEL above Lake Cushman

## Slide 6
Ground-based measurements on NE side of the Olympics
  Good surface infrastructure at Hurricane Ridge
  Can be covered by the Canadian radar sited on Vancouver Island
  Covers the N and NE side of the snowfield

## Slide 7
Ground-based measurements on SW side of the Olympics
  NPOL siting…have found a site! …sees both ocean and Olympic Mountains
  Snow depth measurement testing at remote sites…good results
  Rain gauge network in the Quinault region tested and data analyzed
  Identification of 3 remote locations for remote precipitation amount and particle size distribution measurements, to be tested this year
    Power, access, instrument performance
    Major test to be done at Snoqualmie Pass…equipment being prepared…to determine feasibility for work in the Park

## Slide 8: Radars
WSR-88D at Langley Hill
NPOL & DR3 on coast near Taholah
Canadian X-Band on Vancouver Island
DOW proposed to be in Quinault to fill in below lowest NPOL elevation angle
ARO reinstalled???

## Slide 9: NPOL site survey
To get there:
Going north on 109 from Moclips, go past the Moclips Highway, about 1-2 mile later is Shale Road marked with a hand painted sign. (On Google Earth it’s called Orville’s Landing Road)

## Slide 10: NPOL site survey
Shale Road 3: What it looks like on the ground. Ele. 455’ 47°16’31.9”N 124°12’32.6”W
N
N
S
S
E
W
Olympics
Very open, 360° view. Excellent view to the Olympics and coast. Local high point on hill to the NW, very little blockage by trees. Wide open spot. May need to level ground and cut down undergrowth. Some cell reception.
Coast

## Slide 11: NPOL site survey
Shale Road 3: Radar blockage. Elevation 455’ 47°16’31.9”N 124°12’32.6”W
Not sure if Zebra sees the hill to the immediate northwest of the site.
This land belongs to the Quinault Nation. We are talking with them about leasing the land for the OLYMPEX project.

## Slide 12: Rain Measurements in the Olympics
Network includes several sites in variable terrain across the ridge between the Quinault and the Queets
Includes 2 coastal stations
Data collected multiple seasons
Results from this past winter:
A) Tipping Bucket Rain Gauge Network

## Slide 13
Some stations removed since they stopped reporting in the middle, or have questionable data due to siting issues (large trees, etc.)

## Slide 14
Closer examination of one rain event January 10 – 12, 2014.
IR satellite image 0000 UTC 10 Jan 2014

## Slide 15
Base reflectivity from LGX, Langley Radar at 0943 UTC 11 Jan 2014
Front is offshore approaching the Olympics. Steady rain already seen on the windward side of the Olympics

## Slide 16
235º
270º
180º
235º
265º
Quillayute Sounding Data
1828
1000
1219
1219
914
850 mb Wind Direction
0°C isotherm height (m)

## Slide 17
Rainfall enhanced on windward side of ridge and in the interior where the station feels the effect of the ‘whole’ Olympic mountain range

## Slide 18: Enhanced Rain/Snow Measurements in the Olympics
Enhanced sites may include Micro Rain Radars (MRR), dual rain gauges, microphysical measurements from 2DVD and Parsivel disdrometers or PIP,
Some locations picked due to power availability (Neilton Pt., near Bunch Field)
Sample at a variety of elevations to observe the rain/snow transition
May want to sample up an NPOL transect (i.e. along the Quinault River)
B) Proposed locations for enhanced ground measurements
= proposed locations for enhanced observations

## Slide 19: Enhanced Rain/Snow Measurements in the Olympics
At Wynoochee, plan to test an APU (parsivel + pluvio) run on solar panels and batteries
At elevation of rain/snow transition.
Exact site TBD
C) Wynoochee test site 2014-15
= proposed locations for enhanced observations

## Slide 20: Snow Measurements in the high terrain of the Olympics
Existing SNOTEL sites have Snow Depth, SWE, temperature
Hurricane Ridge is a NW Avalanche center site and it has Snow Depth, SWE, temperature and winds.
We will install and test out this winter additional instruments at Hurricane: PIP, Hotplate, Parsivel and MRR
Snow Cameras will be installed to monitor snow depth and infer SWE at locations unmeasured before.

## Slide 21: Hurricane Ridge 2014-15 Test site
This winter, we will test out several microphysical instruments that require power at the Hurricane Ridge location: PIP, MRR, Hotplate and Parsivel
The locations where we would install instruments include the roof of the Generator House and on the existing towers. These will be placed so they don’t interfere with the Radio Repeater and with the existing instrumentation.
We will work closely with the NPS and NWAC (if necessary) to assure proper installation.
Generator House
Towers with instruments
The PIP instrument

## Slide 22: Snow Cameras in the Olympics
During 2013-2014 season, remote cameras and snow stakes installed at SNOTEL sites to calibrate the camera’s estimate of snow depth vs. SNOTEL estimate of snow depth.
This winter, remote cameras will be placed at 4 study areas (about 3-4 cameras each site) at locations on SW Olympics where measurements have not taken place since 1950’s (from snow surveys)
Snow camera installers and analysists:
Adam Massman, Derek Beal, Teddy Thorson

## Slide 23: Snow depth = comparable (differences, which are <<10%, explained by within-site variability)
RMSE: 11.1 cm
Mean bias: Snow Pole 5.4 cm deeper than Snotel Acoustic Sensor
Mean absolute value difference: 8.5 cm

## Slide 24: Tested 3 methods to estimate snow density to achieve SWE:
SNOTEL mean = 0.4
SNOTEL daily = snow pillow weight/depth at SNOTEL, and
Expected seasonal climatology (from Sturm et al. 2010)
Some issues with an intense, cold snow event

## Slide 25: Deployment 2014-15 in Progress: 18 new sites in headwaters of Quinault and Chehalis

## Slide 26: Precipitation event (snow) + Accumulation 1 of 2

## Slide 27: Accumulation 2 of 2

## Slide 28: Snow Measurements in the Olympics
Want to instrument the Low Divide Ranger station with an APU during the experiment.
Testing this idea with a ‘mock up’ of the cabin and batteries/generator at Snoqualmie Pass (Cascades) this winter 2014-15
Low Divide

## Slide 29: Low Divide
Low Divide – elevation ~3500’ is a 2-day hike in – can be dicey in winter
Instruments and batteries will need to be placed there via helicopter
Need to test how long APU can operate unattended
Low Divide Ranger Station

## Slide 30: Low Divide mock-up will be at Snoqualmie Pass in the Cascades
1-hr drive from Seattle, so easy to access to monitor tests
Will have a trailer to act as the ranger station
Will test how long APU can operate unattended, how many batteries are necessary, how often a generator needs to be run, etc.

## Slide 31
Summary of current activities
  Testing out instrumentation performance in difficult environments
    Hurricane Ridge: PIP, Hotplate, MRR, Parsivel
    Mock-up of Low Divide
    Feasibility of operating a APU on solar power in cloudy environments like Wynoochee or Bunch Field
  NPOL location identified
    Negotiations still needed to secure site
  Snow Cameras being installed as we speak
    Last year’s data looks very good
    4 trips planned in the next two months

## Slide 32
To be addressed in coming months
  Aircraft coordination
    DC-8, Citation
    Possible others TBD
    Single point of contact for all aircraft
  Operations center
    Location identified
    Needs to be designed
  Chehalis rain gauge network

## Slide 33
End
  Supported by NASA grants NNX13AG71G, and NNX12AL54G