## Slide 1: OLYMPEX: A Ground-Validation Field Campaign for the Global Precipitation Mission (GPM) Satellite on the Olympic Peninsula in the Pacific Northwest
Lynn McMurdie, Robert A. Houze, Jr., Jessica Lundquist, Cliff Mass, University of Washington, Walter Petersen NASA/Wallops, Mathew Schwaller NASA/Goddard, William Baccus, National Park Service
Pacific Northwest Weather Workshop, Seattle, WA 27 February, 2015

## Slide 2: OLYMPEX
Precipitation is difficult to measure accurately
  Precipitation results from multi-scale processes
  Lack global coverage of ground-based instrumentation – gauges, radars – especially in remote regions
  A good way to fill-in the gaps in surface measurements is to use satellite-based precipitation estimates
The core satellite of the Global Precipitation Measurement (GPM) mission was launched at 1837 UTC 27 February 2014 (0337 JST 28 February) from the JAXA Tanegashima Space Center on Tanegashima Island, Japan.

## Slide 3: The Core Satellite of GPM
The core satellite of GPM is a Polar Orbiting satellite sampling from Antarctic circle to Arctic circle
Non-sun synchronous orbit – crosses the equator at variable local times
Prior generation TRMM only sampled tropical regions
GPM officially means a consortium of precipitation measuring satellites (DMSP, NOAA) which together sample the globe frequently. At any given location, may have 8 overpasses
GPM
TRMM

## Slide 4: The Core Satellite of GPM – Updated Instruments
Dual Precipitation Radar (DPR)
  measures 3-D structure of precipitation
  Ku-band (245 km width swath) and Ka-band (120 km width swath)
  Sensitive to a range of precipitation intensities
GMI
DPR
GPM Microwave Imager (GMI)
  Passive microwave instrument
  904 km swath width
  Has frequencies sensitive to falling snow

## Slide 5: GPM
GPM Goals
  Measure rain and snow globally
    Wide range of intensities: from 0.2 mm/hr to 110 mm/hr
    Wide range of locations: From ocean to complex terrain
    Wide range of regimes: Tropical rainfall to high latitude snowfall
  Apply to high impact events
    Monitoring flood, droughts
    Monitor water supply
Need a Ground Validation (GV) Field campaigns to ensure success
  Test assumptions used in algorithms
  Calibrate satellite estimates of precipitation
  Prior field campaigns done in summer convective regimes, or winter-time light snow regimes
  Has not been done for winter-time synoptic-scale storm systems with rain/snow and in complex terrain: Olympic Mountains in Washington the perfect place.

## Slide 6: The Climatology of the Olympic Peninsula
Persistent moist onshore flow produces extraordinary annual precipitation totals
2500 mm (100”) on the coast and more than 4570 mm (180”) in the interior
Climatology of MSLP from Nov-Feb from NCEP Reanalysis grids 1979 – 2012
Annual average precipitation in inches from PRISM (Parameter-elevation Regressions Independent Slopes Model)

## Slide 7: Climatology of Olympic Peninsula
Rainiest months: Nov, Dec, Jan. Range from 3.5” (90 mm) to 30” (750 mm) in Nov.
On any given day in Nov, Dec, Jan there is a 73% probability of receiving >0.01” rain and a 36% probability of receiving > 0.5” rain.
Monthly Average Precipitation
Clearwater

## Slide 8: Climatology of Olympic Peninsula
KUIL
Mean 0°C level in winter during moist onshore flow = ~1.5 Km
This varies a lot from storm to storm and within each storm.

## Slide 9: Typical Frontal Passage Three different regimes!
Prefrontal
Frontal
Postfrontal

## Slide 10: Typical Frontal Passage Three different regimes!
SW side of Olympics gets rain well ahead of front
SW side gets rain during front
SW side gets post-frontal showers
Prefrontal
Frontal
Postfrontal

## Slide 11: OLYMPEX: Goals
Physical validation of the precipitation (rain and snow) algorithms for both the GMI and DPR.
How precipitation mechanisms in all 3 sectors of midlatitude frontal systems and their modification by terrain affect GPM rainfall estimation uncertainties.
Quantifying the accuracy and uncertainty of the GPM precipitation data and its hydrologic applicability.
Merging numerical modeling and satellite observations to optimize precipitation estimation in hybrid monitoring systems of the future.

## Slide 12: How to achieve these goals?
Physical validation of precipitation algorithms
  Rainfall characteristics – Dropsize distribution, crystal size/habit, rainfall intensity
  Changes in Rain/snow distribution and characteristics as frontal systems move from ocean to coast to steep terrain
  Melting level variability – within individual storms and from storm to storm
  Environmental characteristics – profiles of temperature and humidity
Applications to high impact events
  Snow pack accumulation
  Hydrological response
How are we going to do that?
  Ground instrumentation (precipitation gauges, microphysical instruments, snow cameras, snow surveys) Oct. 2015 – April 2016
  Ground-based weather radars, Nov. 2015 – Dec. 21, 2015 and Jan 2 – 15, 2016.
  Aircraft-based measurements Nov. 6, 2015 – Dec. 21, 2015.

## Slide 13: Geographical Regions
Quinault
Chehalis
Ocean - offshore
High Terrain
Leeside
Windward side – Quinault area and Chehalis

## Slide 14: Ground Instrumentation Overview
Legend
= WSR-88D
= NPOL
= DOW
= EC X-Band
= MRR = SNOTEL
= Ground Obs sites
= Snow camera network = UW Tipping bucket network
= Chehalis rain gauge network
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 15: Ground Sites--Windward side of Olympics/Quinault Valley
Arranged along Quinault River Valley to examine precipitation enhancement and changes in precipitation character as storms encounter higher terrain.

## Slide 16: Ground Instruments – Tipping Bucket Networks
Rain Gauges
Tipping Bucket style (single and Dual)
Need to be in lower elevations
Chehalis will also have 10 – 15 dual Gauges along with CoCoRahs sites

## Slide 17: Ground Instruments – Measuring Rain
Low Elevations Sites with Power can have:
- Micro Rain Radar (MRR)
- Parsivel (distrometer)
- 2DVD
- Rain gauge (dual bucket)
Low Elevation Sites without Power can have:
- Parsivel (powered by solar panel/battery)
- Rain Gauge (dual bucket)
Parsivel MRR
Testing Low elevation site without power at the Quinault Fish Hatchery THIS winter
Trouble with condensation in electronics, some trouble with ‘computer’

## Slide 18: Ground Instrumentation Radar
Legend
= WSR-88D
= NPOL
= DOW
= EC X-Band
= MRR = SNOTEL
= Ground Obs sites
= Snow camera network = UW Tipping bucket network
= Chehalis rain gauge network
x
Soundings
At NPOL site with CSU sounding unit
Extra sounds at UIL?

## Slide 19: Ground Instrumentation Radar
Scan Strategies:
NPOL: RHI scans up Quinault Valley and over Ocean
DOW: Placed up valley to document precipitation growth ‘under’ NPOL bean
X-Band: Scan ‘Lee side’ transition (RHI)
MRR’s: 3 Placed in Quinault to document precip growth in lowest levels
Not doing dual doppler

## Slide 20: High Terrain Measurements
For measuring snow depth and SWE of accumulating snowpack and for measuring falling snow microphysical characteristics
  SNOTEL sites (existing sites)
  Snow Cameras (Lundquist)
  Additional Snow surveys at cameras
  Hurricane Ridge installation
  Enchanted Valley Installation
We are testing strategies this winter

## Slide 21: Snow Camera Installations 2014 - 2015
Jessica Lundquist’s crew installed 18 Cameras and Snow Poles at various locations near historical snow course locations and along the Quinault River and tributaries.

## Slide 22: Precipitation event (snow) + Accumulation 1 of 2

## Slide 23: Accumulation 2 of 2

## Slide 24: Hurricane Ridge
This winter have a collection of 4 specialized instruments installed on the roof of the generator house at Hurricane Ridge
  MRR, Parsivel, PIP and Hot Plate
  Collecting data, but have not analyzed it
Why at Hurricane?
  Only location at high elevation with power available
  Supports the radar measurements made by Canadians on Vancouver island
Maintenance:
  Snow/rime removal
  PIP alignment/bulb replacement
Notes: Example: PIP bulb burned out

## Slide 25: High Elevation Ground Sites – No Power
Want to put instruments to measure precipitation at 2 very remote sites with no power: North Wynoochee (3000+ ft), Upper Quinault Valley (2200+ ft)
Requires mountain biking and snowshoe to access site. Needs to operate 2 weeks unattended
Requires 13 mile hike in winter conditions. Needs to operate 2 weeks unattended

## Slide 26: Testing this year for high elevation installations with no power – Trailer at Snoqualmie Pass
15 ft trailer anchored to ground with 8 deep-cycle batteries, electronics, computer inside
Solar panel to recharge batteries
Pluvio and Parsivel mounted to be ‘above’ snowpack
Testing
  how long batteries can last
  How long instruments can operate in snowy environment
  how often is maintenance needed

## Slide 27: Aircraft
Satellite Simulator instruments
Dropsondes over the ocean
Flies at ~30,000 ft
DC-8
ER-2
Citation
Satellite Simulator instruments and Flies at ~60,000 ft
Cloud Microphysics instruments
Flies at 2000 ft above highest obstacle

## Slide 28
Citation
DC-8
ER-2
NPOL
X-band
Sample Flight Patterns
Citation
dropsondes
Spiral ascent

## Slide 29: Summary
OLYMPEX is a ground validation campaign for the GPM satellite that will occur Fall 2015 thru Winter 2016
OLYMPEX primary objective is to measure and document the characteristics of rain/snow from ocean to coast to complex terrain.
Will have installations of ground instruments at a variety of elevations and locations to measure rain/snow amounts and precipitation characteristics
High terrain measurements include snow cameras, 2 installations of sophisticated instruments where power is available, and 2 installations running on batteries/solar.
There will be 2 radars and 4 upper-looking micro radars and one DOW. Operations Nov 1 – Dec 21, 2015 and Jan 3 – 15, 2016.
There will be 3 aircraft from Nov 6 – Dec 21, 2015 that will fly during intensive observation periods when we have approaching storm systems (complicated operations).

## Slide 30: Ground Instruments – Measuring Rain
Dropsize Distribution
Rain rate and reflectivity
Typical light rainfall event: Lots of small drops. We suspect that the current Q-C software for Parsivel is throwing out the very small drops. Parsivel is under reporting precipitation compared to gauge.

## Slide 31: Climatology of Olympic Peninsula
Longest period with continuous rain (daily precip >=0.01”) = 49 days – Dec 1982.
Probability of 2 week period receiving >= 16” (~400mm) = 4%
Longest ‘dry’ period with daily precip <=0.05”) = 18 days – Dec 1985.
Probability of 2 week period of <= 0.10 (~2.5 mm) during Nov-Feb = 0.25%
Clearwater Wet Spells Nov - Feb
Clearwater Dry Spells Nov - Feb

## Slide 32: Ground Sites – NPOL Radar
Will be installed on the Quinault Indian Nation near the coast along Shale Road where the radar has clear views towards the Ocean and towards the Olympic Mountains and up the Quinault River
Ocean View
Olympics
NPOL
D3R

## Slide 33: Ground Sites– Doppler on Wheels (DOW)
Will be installed at Lake Quinault so it can make measurements where it will sample ‘under’ the lowest radar beam. It will have a horizontal extent of roughly 40 km (can ‘see’ to NPOL and can ‘see’ to Upper Quinault Valley installation.

## Slide 34: Buckinghorse SNOTEL plot this year
Total falling precipitation so far this year = ~105” or 2667 mm
Current Snow water equivalent = 5” or 127 mm.

## Slide 35: Waterhole SNOTEL plot this year
Total falling precipitation so far this year = ~70” or 1778 mm
Current Snow water equivalent = 2” or 51 mm.

## Slide 36: Testing this year for high elevation installations with no power – Trailer at Snoqualmie Pass
Rainy/cloudy/snowy periods – batteries can’t recharge via solar
Joe knocked off snow/ice on solar panel and sunny period recharged
Batteries can continue to operate instruments with less voltage than this
Have not had to use generator yet – batteries operating for 3 months
Morning Battery Status
If completely cloudy/rainy and no solar, looks like batteries can operate instruments for 4 – 6 weeks without recharging – will test this out this summer

## Slide 37
Example from trailer – Wet event

## Slide 38
Example from trailer – Wet event