## Slide 1: OLYMPEX: Ground Validation on the Olympic Peninsula in the U. S. Pacific Northwest
Robert Houze, Lynn McMurdie, Jessica Lundquist, Cliff Mass, Joe Zagrodnik, William Baccus, Walter Petersen, Matthew Schwaller
7th GPM GV Meeting, Seoul, 14 May, 2015

## Slide 2
Olympic Peninsula

## Slide 3: Regimes
Quinault
Chehalis
Ocean
High Terrain
Leeside
Windward side

## Slide 4: The Climatology of the Olympic Peninsula
Persistent moist onshore flow produces extraordinary annual precipitation totals
2500 mm (100”) on the coast and more than 4570 mm (180”) in the interior
Climatology of MSLP from Nov-Feb from NCEP Reanalysis grids 1979 – 2012
Annual average precipitation in inches from PRISM (Parameter-elevation Regressions Independent Slopes Model)

## Slide 5: Rain Forest Climate
Average rainfall during Nov, Dec and Jan is 400 mm (16”) each month. Range is 75 – 750 mm (3 – 30”) from 98 years of data.
Probability of receiving at least 2.5 mm (0.1”) of precip
OLYMPEX

## Slide 6: Typical Frontal Passage Three different regimes!
Prefrontal

## Slide 7: Typical Frontal Passage Three different regimes!
Frontal

## Slide 8: Typical Frontal Passage Three different regimes!
Postfrontal

## Slide 9: Typical Frontal Passage Three different regimes!
SW side of Olympics gets rain well ahead of front
SW side gets rain during front
SW side gets post-frontal showers
Prefrontal
Frontal
Postfrontal

## Slide 10: OLYMPEX objectives
Observe all 3 sectors of frontal systems
Observe passage from ocean to coast to upslope to leeside
Determine how precipitation processes vary between sectors
Modification of processes by terrain
Hydrology
Model experiments

## Slide 11: Network Overview
Legend
= WSR-88D
= NPOL and D3R
= DOW
= EC X-Band
= MRR = SNOTEL
= Ground Obs sites
= Snow camera network = UW Tipping bucket network
= Chehalis rain gauge network
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
DC-8
ER-2
Citation

## Slide 12: Two Rain Gauge Networks
Chehalis
Quinault Valley
10–15 dual gauges CoCoRahs sites
Coop observers
Single bucket gauges

## Slide 13: Radars

## Slide 14: NPOL/D3R Radar Site
On Quinault Indian Nation land near the coast where the radar has clear views towards the Ocean and towards the Olympic Mountains and up the Quinault River
Pacific Ocean (SW)
Olympic Mts. (NE)
NPOL
D3R

## Slide 15: Radar coverage
Scan Strategies:
NPOL: RHI scans up Quinault Valley and over Ocean
D3R: TBD
DOW: Scan up and down valley to document precipitation growth ‘under’ NPOL beam
X-Band: RHI scans over Hurricane Ridge on leeside
MRR’s: Placed to document precip growth in lowest levels

## Slide 16: Doppler on Wheels (DOW)
Will be installed at Lake Quinault so it can make measurements where it will sample ‘under’ the lowest NPOL radar beam. It will have a range of ~40 km (can ‘see’ to NPOL and can ‘see’ to Upper Quinault Valley installation.

## Slide 17: Ground instruments

## Slide 18: Ground Instrument Sites For Rain
Low Elevations Sites with Power
- Micro Rain Radar (MRR)
- Parsivel (disdrometer)
- 2DVD
- Rain gauge (dual bucket)
Low Elevation Sites without Power
- Parsivel (powered by solar panel/battery)
- Rain Gauge (dual bucket)
Parsivel MRR
Testing of Low elevation site without power at the Quinault Fish Hatchery ongoing

## Slide 19: Event Sampled at Quinault Fisheries 27 – 28 March, 2015
Frontal Passage at UIL

## Slide 20: Event Sampled at Quinault Fisheries 27 – 28 March, 2015
Lots of small drops before frontal passage – Reminiscent of White et al. (2003) of non-brightband warm rain processes and like Waldvogel 1974
Droplet size growth at time of frontal passage
Reflectivity similar for prefrontal and frontal regimes
24hr total precip = 20 mm
Post-frontal showers after 0400 UTC
Frontal Passage at APU30

## Slide 21: High Terrain Measurements

## Slide 22: Snow Camera Installations 2014 - 2015
Jessica Lundquist’s crew installed 18 Cameras and Snow Poles at various locations near historical snow course locations and along the Quinault River and tributaries.

## Slide 23: Leeside Station Hurricane Ridge
Coordinated with Env. Canada radar
Has power
Testing during past winter
  MRR, Parsivel, PIP and Hot Plate
  Collecting data, but have not analyzed it
Potential problems:
  Snow/rime removal
  PIP alignment/bulb replacement
  Wind
Notes: Example: PIP bulb burned out

## Slide 24: High Elevation Ground Sites with no Power
Want to put instruments to measure precipitation at 2 very remote sites with no power: North Wynoochee (3000+ ft), Upper Quinault Valley (2200+ ft)
Requires mountain biking and snowshoe to access site.
13 miles by pack animals

## Slide 25: Trailer for high elevation installation at Wynoochee
15 ft trailer anchored to ground with 8 deep-cycle batteries, electronics, computer inside
Solar panel to recharge batteries
Pluvio and Parsivel mounted to be ‘above’ snowpack
Testing
  how long batteries can last
  How long instruments can operate in snowy environment
  how often is maintenance needed

## Slide 26: Also
  NPS snow surveys—seasonal accumulation

## Slide 27: OLYMPEX Summary
Fall 2015 — Winter 2016
Rain and snow over ocean, coast, mountains
Windward side ehancement, leeside suppression
Snowpack buildup and melt off
Two watersheds
Ground instruments at a variety of elevations and locations
Nine radars including NPOL, D3R, & DOW
3 aircraft from 6 Nov – 21 Dec 2015

## Slide 28: Precipitation event (snow) + Accumulation 1 of 2

## Slide 29: Accumulation 2 of 2

## Slide 30: End

## Slide 31: Acknowledgment
This work is supported by the National Aeronautics and Space Administration grants NNX13AG71G & NNX14AO64G

## Slide 32: Climatology of Olympic Peninsula
Average rainfall during Nov, Dec and Jan is 400 mm (16”) each month. Range is 75 – 750 mm (3 – 30”) from 98 years of data.
Probability of receiving at least 0.2mm (0.01”) of precip
Probability of receiving at least 2.5 mm (0.1”) of precip
Probability of receiving at least 12.5mm (0.5”) of precip