## Slide 1: Ground Network Status Gauge & Disdrometer Performance
Joe Zagrodnik
Lynn McMurdie, Robert A. Houze
OLYMPEX Science Meeting
21 March 2017

## Slide 2: Types of Ground Data Available
Precipitation measurement:
  27 Tipping Bucket Rain Gauge Sites
  3 Pluvio Weighing Precipitation Gauges
Disdrometers:
  15 Parsivels (13 APUs)
  2 PIPs
  4 2DVDs
4 Micro Rain Radars
Lots of possible choices, but some data are better than others!

## Slide 3: Rain Gauges
19 “Iowa” Dual-Tipping bucket sites (NASA00xx)
8 “Standalone” Dual-Tipping bucket sites (STDALNxx)
Most sites remained for full 2015-16 winter
Users need to be very careful with data—lots of minor issues.

## Slide 4
View preliminary (non-processed) plots of all ground data online
olympex.atmos.washington.edu

## Slide 5
Choose plot type and time range from drop down menus:

## Slide 6
olympex.atmos.washington.edu
Site status spreadsheet

## Slide 7: Gauge status reported in Google Doc
Yellow: Gauge data is available but calibration appears to be off
Red: Gauge malfunctioning or not tipping
Green: Gauge data is available and gauges "A" and "B" are within ~5% of each other
Gray: Not installed
Blue: No data available
https://docs.google.com/spreadsheets/d/104aJ5bKUXEM_KrD4fqeIE-L2ZR2xjjjH_auXuAZs6co/

## Slide 8
Fairly good calibration
(within 5%)
Poorly calibrated
(8% difference)

## Slide 9
Snow in Gauges
Widespread from 20-Dec-2015 to 10-Jan-2016
Norwood Gauge Flood
17-November-2015

## Slide 10
Steady precipitation incorrectly starts 4 hours early
See Google Doc for specific corrections
Only applies to 3 standalone sites
Appears to be exactly 4 or 5 hour offset

## Slide 11: Pluvios
Three Pluvio sites
Mostly bad data at Neilton Pt (wind, power outages)
Some data missing at Wynoochee and Upper Quinault due to issues with electronics/power supply

## Slide 12: Bucket Not Secured Properly (Wynoochee 05-27 Jan 2016)
Instrument detects 140 mm of precip
Bucket weight remains steady at 400 mm

## Slide 13: Bucket Overflowing

## Slide 14: Bucket Overflowing

## Slide 15: Snow dropping into bucket

## Slide 16: Parsivel (APU)
15 Total Sites
8 sites remained for full 2015-16 winter
Co-located 2DVDs at
  Fishery
  Neilton Pt
  Amanda Park
  Bishop
Raw (10 s) data available on TRMM-FC
Processed (1 min) data – more details in next talk (Ali Tokay)
APU13
APU01
APU04
APU03
APU06
APU05
APU11
APU10
APU02
APU07
APU08
APU09
APU30
HRIDGE
Albert Head, BC

## Slide 17: Issues with Parsivel dataset
Condensation on Optics (#1 problem)
Electronics or Dead Batteries
Snow
Wind is also an issue at exposed sites

## Slide 18: UW “Parsivel Refl” Plots
Issue: Precip type recorded as “ice” (weather code = 88)
Cause: strong winds
Issue: Error Code “3”
Cause: water blocking Parsivel optics

## Slide 19
Also useful for seeing when snow occurred at higher elevations
Raw: includes snow
Processed: snow removed

## Slide 20
Smallest drop bins stop recording drops
If the issue is really bad, all data will be missing
Still raining here—no drops recorded!
“Parsivel PSD” Plots
Error Code 3 present for most of this day

## Slide 21: 2DVD
Co-located with Parsivels (APUs)
All 2DVDs removed in Jan 2016
SN37 (Neilton Point) had major issues with wind, snow, and power outages
See next talk (Ali Tokay) for details.

## Slide 22: MRR
Co-located with Parsivels (all 4 sites), 2DVDs (3 sites), and PIP (2 sites)
Two sites remained for full winter
Hurricane Ridge also has data for most of 2014-15 (test winter)
Raw Spectra is not available at Fishery in Nov-Dec 2015
+PIP
+Parsivel
+PIP
+Parsivel
+2DVD
+Parsivel
+2DVD
+Parsivel
+2DVD

## Slide 23
Built-in Metek “Ave” Data

## Slide 24
Built-in Metek “Ave” Data
Lots of noise in velocity—likely caused by strong vertical motions

## Slide 25: Impact on Processing Algorithms (ImProToo)
Correctly dealiased spectra
17-Nov 0147 UTC
Dealiased Velocity Spectrum
Mask (Blue = accepted data)
Incorrectly dealiased spectra
17-Nov 1249 UTC
Raw Velocity Spectrum
Dealiased Velocity Spectrum
Mask (Blue = accepted data)
Raw Velocity Spectrum

## Slide 26: Summary
Data is excellent for case studies
Be careful with longer-term statistics
Use Google Doc
Use plots on UW OLYMPEX site
Email jzagrod@uw.edu with any questions